## Slide 1: Bayesian Graph Neural Networks, how to optimize a cellular network and provide confidence to our customers
Ericsson Cognitive Software

## Slide 2: How to optimize a cellular network
Optimization
Cellular Network
Solution Architecture

## Slide 3: Uplink Interference
Interference from neighbor cell
Serving eNB
Neighbor eNB
pZeroNominalPusch (p0)
  Target uplink transmission power of UE
  High p0 = high UE throughput, but also higher interference on neighbors
Alpha (a)
  Pathloss compensation factor
  High a = higher UE throughput at cell border, higher neighbor interference

## Slide 4: Use GNN as a digital twin
Relation information:
- Physical distance
- Traffic exchanged
- Footprint overlap
- Relation parameters
Performance metrics
Configuration
A
B
C
D
E
F
Digital Twin
Apply Graph Neural Network (GNN) to accurately model radio cellular network relations & configurations
Encode Network Data
Generic parameter framework to emulate effect on network performance indicator
Accurate modeling of real cellular network behavior
GNN architecture provides a native way of modelling cellular network interactions. The framework being developed will make the optimizer development process very straight forward and intuitive.
Digital Twin
GNN optimizer modelling enable the finding of the optimal configuration without the need of interacting with the live network by emulating radio network performance functionality from real network data

## Slide 5: Optimization Framework
1. Predict SINR with
current parameters
2. Alter power parameters until
predicted SINR is maximized
[-92, 9]
[-88, 9]
13
14
20
16
15
2. Predict SINR with
new parameters
1. Alter power parameters
Test Configuration
(Including Performance KPIs)
[-110, 8]
[-106, 9]
[-80, 8]
[-90, 10]
[-100, 10]
[-120, 10]
[-103, 10]
Issue cell
Issue cell
Predicted UL SINR
20
18
10
21
8
17
17
Trained GNN Model

## Slide 6: How are our predictions perceived by customers?
Unreliable prediction
Reliable prediction
Lack of confidence

## Slide 7: How can we solve the lack of confidence?
Give single predictions
Give specific confidence intervals for each prediction
Prediction
Prediction
Prediction

## Slide 8: How can we transform our models to give confidence intervals?

## Slide 9: Inference in Bayesian Neural Networks

## Slide 10: The application to cellular data, Bayesian Graph Neural Network

## Slide 11: Optimization Framework v2
1. Predict SINR with
current parameters
2. Alter power parameters until
predicted SINR is maximized
[-92, 9]
[-88, 9]
13
14
20
16
15
2. Predict SINR with
new parameters
1. Alter power parameters
Test Configuration
(Including Performance KPIs)
[-110, 8]
[-106, 9]
[-80, 8]
[-90, 10]
[-100, 10]
[-120, 10]
[-103, 10]
Issue cell
Issue cell
Predicted UL SINR
20
18
10
21
8
17
17
Trained Bayesian GNN Model